- Apply constraints in first time step – remove and apply different ones for geometry changes
- In NSE constraints for PRESSURE, VELOCITY_X, VELOCITY_Y, VELOCITY_Z
- linear solver: always AMGCL, standard for NSE,
  NOTE: stating “amgcl” explicitly uses higher tolerance than stating no linear solver!

MLS shape functions

Static heat test case
- rectangular domain, refinement 0, h=0.2, cut at y=0.8+-1e-12
- density, specific heat, conductivity = 1
- T=x²+y² boundary condition, source term = -4
- error evaluated at Gauss points using only ACTIVE element (positive level set distance, not cut)
- conditioning evaluated using eigenvalues lamda_max/lamda_min
- DistMod → instability for small cut on positive side (+1e-12)
- LocalConstraintsBC → instability for +1e-12 (like DistMod), same as constraining directly to BC for -1e12
- LocalMLSConstraints → instable, error: zero sum in skyline_lu factorization

NSE test cases